## Slide 1: Vertical Axis Wind Turbine Performance Prediction
via Artificial Neural Network
Batuhan Atasoy, Ezgi Demir, Oğuz Susam
MAK 660 E
2021 ITU

## Slide 2: Outline
Aerodynamics of H-rotor Turbines
Performance Evaluation of H-rotor Turbines
The Numerical Method
The Database for First Analysis
The Database for Second Analysis
Results of NNtool
Results of TensorFlow
Conclusions

## Slide 3: H-rotor Turbines
(A) Savonius turbine: Drag Driven
(B) Darrieus turbine: Lift Driven
(C) H-rotor(Straight Bladed Darrieus) turbine: Lift Driven
Picture : Eriksson, S., Bernhoff, H. ve Leijon, M. (2008). Evaluation of different turbine concepts for wind power, Renewable and Sustainable Energy
Reviews, 12(5), 1419 – 1434, http://www.sciencedirect.com/science/article/pii/S1364032107000111.

## Slide 4: Aerodynamics of H-rotor Turbines

## Slide 5: The Performance Curves
Power Coefficient: Power of wind / The torque generated on the blades * angular velocity
Cp ----> efficiency!!!
TSR : linear velocity of the blades / Uinf
Picture : Eriksson, S., Bernhoff, H. ve Leijon, M. (2008). Evaluation of different turbine concepts for wind power, Renewable and Sustainable Energy
Reviews, 12(5), 1419 – 1434, http://www.sciencedirect.com/science/article/pii/S1364032107000111.

## Slide 6: The Numerical Method
Potential Flows based on some assumptions
  Irrotational
  Inviscid ( alike non-frictional)
  Linear
Double multiple-streamtube model (DMST)
Advantages
  3D (in Qblade even more developed, some semi empirical corrections)
  CHEAP!!! (in CFD, a 2D analysis can be completed 1-2 days with a standart laptop)
Disadvantages (in comparison with CFD)
  Inviscid
  Non-turbulent
  Overprediction
  Unsatisfied results at extreme TSRs because of lackness of dynamic stall model and turbulent model
QBlade 64bit v0.963 (Berlin TU)

## Slide 7: Data Generation-I
Flow Parameters
  TSR (1~7, 0.25)
Global Parameters
  Blade Number (2,3,4)---->classes
  Rotor Diameter (0.5, 1, 1.5, 2) ----->classes
Foil Geometry
  sigma
    chord length/rotor diameter
    0.18-0.72
  tau
    blade thickness/chord length
    0.12-0.21Ref:SPC307-Introduction to Aerodynamics
Output: Cp
Picture : Eriksson, S., Bernhoff, H. ve Leijon, M. (2008). Evaluation of different turbine concepts for wind power, Renewable and Sustainable Energy
Reviews, 12(5), 1419 – 1434, http://www.sciencedirect.com/science/article/pii/S1364032107000111.

## Slide 8: ANN with NNtool
1 input, 3 hidden and 1 output layers
activation fun.s are TANSIG and PURELIN
optimizer : GDM
loss : mse
max_fail : 100

## Slide 9: NNtool
Feed-forward backpropagation
Training function
  Levenberg-Marquardt
  Scaled-conjugate gradient
Learning function
  Gradient-descent momentum
Training evaluation
  MSE : metric
  Max_fail no. in validation : preventing overfit :6, 100, 150
  Linear regression
Number of neurons in hidden layer
  5,10
Number of layers
  1,3
DATA
3975 samples
  part. ratio : %70
    train: 2783
  part. ratio : %80
    train: 3179
  part. ratio : %90
    train: 3577
with a data manipulation (Cp>0)
with a data manipulation (Cp>0.01)

## Slide 10: NNtool-Part. Rat %100
Training function
  Scaled-conjugate gradient
Learning function
  Gradient-descent
Training evaluation
  MSE :
  Max_fail no. in validation : 6
Number of neurons in hidden layer
  5
Number of hidden layers
  1

## Slide 11: NNtool-Part. Rat %100
Training function
  Levenberg-Marquardt
Learning function
  Gradient-descent
Training evaluation
  MSE :
  Max_fail no. in validation : 6
Number of neurons in hidden layer
  5
Number of layers
  1

## Slide 12: NNtool-Part. Rat %100
Training function
  Levenberg-Marquardt
Learning function
  Gradient-descent momentum
Training evaluation
  MSE :
  Max_fail no. in validation : 6
Number of neurons in hidden layer
  10
Number of layers
  1

## Slide 13: NNtool-Part. Rat %100
Training function
  Levenberg-Marquardt
Learning function
  Gradient-descent momentum
Training evaluation
  MSE :
  Max_fail no. in validation : 6
Number of neurons in hidden layer
  10
Number of layers
  3

## Slide 14: NNtool-Part. Rat %100
Training function
  Levenberg-Marquardt
Learning function
  Gradient-descent momentum
Training evaluation
  MSE :
  Max_fail no. in validation : 100
Number of neurons in hidden layer
  10
Number of layers
  3

## Slide 15: NNTool- Part. Rat. %70-R

## Slide 16: NNTool- Part. Rat. %80-R

## Slide 17: NNTool- Part. Rat. %90-R

## Slide 18: NNtool- Loss functions

## Slide 19: ANN with TensorFlow
1 input, 3 hidden and 1 output layers
activation fun.s are tanh and relu
optimizer : adam
loss : mse
metrics : mse

## Slide 20: ANN with TensorFlow

## Slide 21: ANN with TensorFlow
Correlation matrix enables us to see the collinearity of the data, so it enables to select the features having a correlation of less than 0.85.

## Slide 22: ANN with TensorFlow
One another important thing is, we used two-way Hypothesis tests to separate the train data as a sample to give information about the population.
To perform this, we developed a Hypothesis Testing such that,
Assumptions:
The number of train data is much greater than 30, so z-score must be employed.
We know the sample (train dataset) mean and variance.
So, the retain condition for Hypothesis tests becomes,

## Slide 23: TensorFlow- Part. Rat. %70-R

## Slide 24: TensorFlow- Part. Rat. %80-R

## Slide 25: TensorFlow- Part. Rat. %90-R

## Slide 26: TensorFlow- Loss functions
After 2500 epochs, the loss function approaches 10^-4 interval, as given in figure below:

## Slide 27: TensorFlow- Loss functions

## Slide 28: TensorFlow- Results for cl=0.1
At the second part of the analyses, we used cl=0.1 data and cl=0.2 data to validate our model:

## Slide 29: TensorFlow- Results for cl=0.2

## Slide 30: Conclusions
Numerical Method
  it is very fast
  convenient to generate data in preliminary stages
  the study can be expanded with CFD and turbulent models
  method can be developed with semi-empirical dynamics stall models such as Beddoes-Leishman model
ANN model
  The best results obtained by Levenbert Marquardt training function
  Also SCG model gives acceptable results (R>0.92)
  Although the one hidden layer is satisfied, but increasing the layer numbers made the model exceptional (R from 0.96 to 0.99)

## Slide 31: Conclusions
Tools
  The model was trained in about 150-200 epochs for MATLAB, 2500 epochs for Python
  NNtool is very simple to use
  On the other hand, TensorFlow more sophisticated tool and it requires moderate Python skills
  TensorFlow is FREE!!
  With the help CUDA-support, TensorFlow can also handle big data and much more sophisticated hidden layers and neurons.
Future works and Utilization in real life
  Capability of ANN to predict wind turbine performance
  Necessity of ANN modeling as a metamodel
  Neuro-Fuzzy methods in turbine control and blade design

## Slide 32: Thank you for listening!